## Slide 1
Day 2: Timers, Counters &
Troubleshooting
Day 2 — Timers, Counters & Troubleshooting
1

## Slide 2
Session Roadmap
Block | Topic | 
1 | Timers: TON, TOF | 
2 | Counters (CTU, CTD) + Edge Detection | 
3 | Online Monitoring & Forcing I/O | 
4 | Combine Timer + Counter, Group Troubleshooting | 
5 | Day Project — Traffic Light Controller | 
Day 2 — Timers, Counters & Troubleshooting
2

## Slide 3
Addressing Convention Used Throughout
Adjust to whatever platform the lab actually runs — Allen-Bradley/RSLogix, Siemens TIA/S7, or CODESYS/IEC 61131-3 generic.
Platform | Input bit | Output bit | Internal / Memory
IEC generic | %I0.0 | %Q0.0 | %M0.0 (bit), %MW10 (word)
Allen-Bradley | Start_PB (tag) | Motor_Run (tag) | Tag-based — no raw address needed once tags are used
Siemens | I0.0 | Q0.0 | M0.0, MW10, DB1.DBX0.0 (data-block bit)
Day 2 — Timers, Counters & Troubleshooting
3

## Slide 4
Block 1
Timers: TON, TOF
30 minutes

## Slide 5
1A · 12 MIN
TON — Timer On-Delay
TON_Instance(IN := StartCondition, PT := T#5s);
Q := TON_Instance.Q; // BOOL, true when ET >= PT
ET := TON_Instance.ET; // TIME, elapsed time, counts up while IN = TRUE
Parameter | Type | Meaning
IN | BOOL | The timer's enable / input condition
PT | TIME (IEC) / DINT ms (AB) | Preset — e.g. AB uses DINT 5000 for 5 seconds
ET | TIME / DINT (.ACC on AB) | Accumulated value; counts up in ms while IN is true
Q | BOOL | True once ET ≥ PT, false otherwise
Day 2 — Timers, Counters & Troubleshooting
5

## Slide 6
1A
TON — Internal State Machine
IF IN = TRUE THEN
IF ET < PT THEN
ET := ET + (time since last scan)
END_IF
IF ET >= PT THEN
Q := TRUE
END_IF
ELSE
ET := 0
Q := FALSE
END_IF
Note: ET accumulates by actual elapsed wall-clock time between scans, not a fixed "one tick per scan" — this is why timer accuracy is largely independent of scan-time variation.
A platform typically uses a hardware clock/counter for this, not scan-count — unlike a naively-implemented counter, which is genuinely scan-dependent (relevant again in Block 2c).
Day 2 — Timers, Counters & Troubleshooting
6

## Slide 7
1A
TON — Timing Diagram & Ladder Rung
IN ___/‾‾‾‾‾‾‾‾‾\________/‾‾‾\___
ET ___/‾‾‾‾‾\____0________/‾\__0_
PT reached IN drops before PT
Q _________/‾‾‾\__________________
(Q never asserts on 2nd pulse — IN dropped before PT)
|--[ Start_PB ]------------------( TON )--|
Timer: MotorDelay
Preset: 5000 (ms)
Accum: 0
Rule: ET resets to 0 the scan after IN goes false — it is not held or paused. Non-negotiable for a standard (non-retentive) TON; this is what distinguishes it from the RTO in Block 4a.
Analogy: a kitchen timer that only counts while you hold the start button — release before it dings and it resets to zero.
Day 2 — Timers, Counters & Troubleshooting
7

## Slide 8
1A
TON — Live Demo & Precision Note
Live demo: wire the TON so Q drives a lamp output, 5-second PT. Open the data monitor and watch .ACC / ET tick upward in real time (commonly 1ms or 10ms resolution).
Show a full-duration hold (Q asserts) and an early release (ET snaps back to 0, Q never asserts).
Run a third variant: release right at the boundary (e.g. 4.9s of a 5s preset) — "almost done" still means "fully reset." No partial credit in this instruction's behavior.
Precision/resolution note: most PLC timer instructions have a stated resolution (e.g. 1ms) separate from scan time.
A timer can, in principle, be more precise than the scan cycle it's evaluated within, since accumulation is driven by a hardware clock — but the observable update of Q and ET is still bound to the next scan's logic-solve phase.
A timer preset of "5000ms" may assert Q on a scan slightly after the 5000ms mark, never before — worth knowing for tight timing tolerances.
Day 2 — Timers, Counters & Troubleshooting
8

## Slide 9
1B · 12 MIN
TOF — Timer Off-Delay
TOF_Instance(IN := MotorRunning, PT := T#30s);
Q := TOF_Instance.Q; // true immediately on IN rising edge,
// stays true PT after IN falls
IF IN = TRUE THEN
Q := TRUE
ET := 0
ELSE
IF ET < PT THEN
ET := ET + (time since last scan)
Q := TRUE
ELSE
Q := FALSE
END_IF
END_IF
Note: Q on a TOF goes true on the same scan IN goes true (zero delay on rising edge) — the delay only applies to the falling edge. This asymmetry is exactly what confuses students in 1d.
Timing diagram: IN rises, Q rises with it. IN falls; Q stays true for the full PT (30s), then falls.
Day 2 — Timers, Counters & Troubleshooting
9

## Slide 10
1B
TOF — Real-World Examples
|--[ Motor_Running ]------------------( TOF )--|
Timer: FanRunOn
Preset: 30000 (ms)
|--[ FanRunOn.Q ]----------------------( Fan_Output )--|
Cooling fan example: the fan keeps running 30 seconds after the motor stops, to dissipate residual heat.
Second example — security floodlight: triggered by a motion sensor, wired so the light stays on for 2 minutes after the sensor last detected motion, rather than switching off instantly (visually jarring, defeats the light's purpose).
Ask the class to identify IN (motion sensor) and what PT should be (120,000ms) before revealing the rung, so they apply the mental model rather than just watching it applied.
Day 2 — Timers, Counters & Troubleshooting
10

## Slide 11
1C – 1D · 6 MIN
Preset Experimentation & Common Mistake
1c — Preset Value Experimentation (6 min)
Have students edit .PRE / PT live (e.g. 5000ms → 2000ms) and re-run the demo, watching ET reach the new value faster.
If the platform supports online edits without a full download, use that to keep iteration fast.
Have a student try an unusually short preset (e.g. 100ms) — Q still asserts reliably as long as PT exceeds one scan's worth of time. Ask: what if PT were shorter than a single scan? (Seeds the idea that scan time imposes a practical lower bound on usable timer resolution — callback to Day 1, Block 3.)
1d — Common Student Mistake (flag proactively)
TON vs TOF direction confusion. Put both timing diagrams on the board and have students point to the exact scan-cycle moment each Q transitions high and low.
Students often assume a TOF's Q starts false and only goes true after the delay — backwards. Q is immediately true on IN going true; only the turn-off is delayed. Say it twice, differently, since the instruction names actively mislead first-timer intuition.
Day 2 — Timers, Counters & Troubleshooting
11

## Slide 12
Block 2
Counters (CTU, CTD)
+ Edge Detection
35 minutes

## Slide 13
2A · 8 MIN
CTU — Count Up
CTU_Instance(CU := PartSensor, RESET := ResetBtn, PV := 10);
CV := CTU_Instance.CV; // INT/DINT, current count
Q := CTU_Instance.Q; // BOOL, true when CV >= PV
Parameter | Meaning
CU | Count-up input, rising-edge sensitive by instruction design (increments once per false→true transition, not while held true)
RESET | BOOL — zeroes CV when true
PV | Preset value (AB: .PRE)
CV | Current accumulated count (AB: .ACC)
Day 2 — Timers, Counters & Troubleshooting
13

## Slide 14
2A
CTU — Internal Behavior & Data Types
Data type note: Allen-Bradley counters typically use DINT (32-bit signed, −2,147,483,648 to 2,147,483,647); Siemens S7 counters (S_CU) are often a native 16-bit counter word, range 0–999.
Internal behavior, precisely: the counter instruction maintains a hidden "previous CU state" bit internally — this is why a raw CTU wired directly to a held-true input does not re-trigger every scan on most platforms; the instruction's own internal edge-detection on CU prevents that.
This sets up Block 2c: the CTU's own count input is edge-sensitive by design, but a plain contact-to-coil rung is not — 2c is about signals feeding into other logic that lacks this built-in edge sensitivity.
Overflow behavior: most CTU implementations do not wrap silently past their data type's maximum — many platforms simply stop incrementing once CV reaches the max representable value. Platform-dependent; check against the lab's specific PLC brand rather than assuming.
Day 2 — Timers, Counters & Troubleshooting
14

## Slide 15
2B · 7 MIN
CTD — Count Down
CTD_Instance(CD := PartRemoved, LOAD := LoadBtn, PV := StartingCount);
CV := CTD_Instance.CV; // decrements toward 0
Q := CTD_Instance.Q; // true when CV <= 0
Contrast the reset semantics explicitly: CTU resets CV to zero; CTD typically loads CV to a starting PV value via a LOAD input rather than "resetting" — different instruction, different parameter name. Don't let students assume symmetry that isn't there.
Combined CTUD note: some platforms offer a single up/down counter instruction — CTUD combines both behaviors into one instance with separate CU and CD inputs sharing one CV.
Worth a one-line mention if the lab platform supports it — common enough in real applications (e.g. tracking net inventory where parts both arrive and leave) that students should recognize the name later.
Day 2 — Timers, Counters & Troubleshooting
15

## Slide 16
2C · 10 MIN
Edge-Triggered Instructions — R_TRIG / F_TRIG
This is the technical core of the whole block. An R_TRIG maintains one bit of internal state — the value of its input from the previous scan. Each scan it compares current input to that stored previous value:
IF (CurrentInput = TRUE) AND (PreviousInput = FALSE) THEN
Q := TRUE // exactly one scan
ELSE
Q := FALSE
END_IF
PreviousInput := CurrentInput
// update for next scan
F_TRIG (mirrored):
IF (CurrentInput = FALSE) AND (PreviousInput = TRUE) THEN
Q := TRUE
ELSE
Q := FALSE
END_IF
PreviousInput := CurrentInput
Why: Q is true for exactly one scan — typically single-digit milliseconds — regardless of how long the physical button stays pressed.
|--[ PartSensor ]--[ONS]----------------( CountPulse )--| (Allen-Bradley: One-Shot / OSR — Rising)
|--[ CountPulse ]---------------------------( CTU )--| (Siemens: P-edge contact, denoted P)
Counter: PartCount Preset: 10
Day 2 — Timers, Counters & Troubleshooting
16

## Slide 17
2C
Concrete Demonstration — Run This Exactly
1. Wire a plain contact from PartSensor (not a counter, to isolate the concept from CTU's own internal edge-sensing) directly into an ADD-and-store rung executed every scan the input is true. Hold the button ~2 seconds. If scan time is ~10ms, that's ~200 scans — the value increments ~200 times for one physical press (subject to scan-time variation).
2. Insert ONS / R_TRIG between PartSensor and the same increment rung. Repeat the same 2-second hold. The value increments by exactly 1.
Narrate live: "Roughly 10ms scan time, ~2000ms hold ≈ 200 scans — that's why you saw the count jump by roughly 200, not exactly 200, since scan time isn't perfectly fixed."
Ask the class to predict, before running it, roughly how many counts a 500ms hold would produce at the same scan rate (~50) — turn it into a quick prediction-then-verify exercise rather than a pure demo.
Day 2 — Timers, Counters & Troubleshooting
17

## Slide 18
2C — TIE BACK TO 2A
Why This Is Distinct From CTU's Own Edge-Sensing
The CTU instruction already debounces its own CU input internally.
The R_TRIG/ONS lesson here is about the general pattern: any rung that increments a value, sets a flag, or triggers an action on every scan a condition is true needs explicit edge detection if the intent is "once per event" — because plain contact-to-coil logic has no built-in memory of previous scans.
This generalizes far beyond counters — it directly resurfaces on Day 3 for alarm/event logging.
Day 2 — Timers, Counters & Troubleshooting
18

## Slide 19
2D · 10 MIN
Project: Edge-Triggered Part Counting
Task: PartSensor (simulated rising edge) → ONS / R_TRIG → CTU with PV=10 → Q drives BatchComplete output; separate ResetBtn → counter RESET.
While circulating, check specifically:
  Is ONS placed before the counter's count input, or mistakenly wired to the reset line? Ask: "What happens if you hold the reset button down as currently wired?" to surface the misapplication if present.
  Does ResetBtn itself need its own edge detection wired to RESET, or is a held-true reset acceptable? Discuss briefly — for a RESET input, holding true generally just holds CV at zero rather than causing repeated miscounting. This is meaningfully different from the CU input case — have students articulate the distinction themselves.
Day 2 — Timers, Counters & Troubleshooting
19

## Slide 20
Block 3
Online Monitoring &
Forcing I/O
25 minutes

## Slide 21
3A · 8 MIN
Watching Live Rung States
Energized rungs/contacts highlight (commonly green, or bold outline) in online/monitor mode.
Have students read a live rung and state the truth value of each contact and the resulting coil state without prompting.
Extend into reading .ACC / ET values directly off timer and counter instructions on-screen — not just their BOOL Q outputs.
Why it matters: This numeric-value monitoring is what actually gets used in Block 4's debugging exercise — make sure students practice locating these fields in the software's instruction display, not just the pass/fail highlight color.
Day 2 — Timers, Counters & Troubleshooting
21

## Slide 22
3B · 10 MIN
Forcing Inputs/Outputs — Mechanism
Forcing intercepts the value between the physical I/O module and the logic engine.
A forced input substitutes a software-set value for the actual voltage read at the terminal; a forced output substitutes a software-set value for what gets written to the physical terminal, regardless of what the logic computed.
Normal: Physical terminal --> Input Image Table --> Logic --> Output Image Table --> Physical terminal
Forced: [FORCED VALUE] --> Input Image Table --> Logic --> [FORCED VALUE] --> Physical terminal
Use cases: testing logic before field devices are wired; isolating whether a fault is in logic vs. physical wiring/sensor (force the input high — if downstream logic behaves correctly, the fault is upstream in the wiring/sensor, not the program).
A second, less obvious use case: commissioning a machine in stages — forcing downstream outputs to verify wiring to actuators before the upstream sensors that would normally trigger them are even installed yet. Common enough on real installation jobs to name specifically.
Day 2 — Timers, Counters & Troubleshooting
22

## Slide 23
3B
Forcing — Platform Behavior & Safety
On many platforms, forces persist even through a program download or a PLC mode change (RUN → PROGRAM and back).
Some platforms display a distinct "FORCE" indicator LED specifically to warn that active forces exist somewhere in the system — because a forgotten force left active from a previous testing session is a genuine, recurring real-world hazard.
State plainly: Always check for and clear active forces before leaving a system in a production state.
Safety caveat: a forced output bypasses interlocks entirely, because forcing happens after the logic solve — overwriting whatever the logic, including any safety interlock rungs, computed.
On a live system this requires lockout/tagout procedures; this is a training/simulator-only exercise as presented here.
Day 2 — Timers, Counters & Troubleshooting
23

## Slide 24
3C · 7 MIN
Reading Fault / Diagnostic Indicators
Module fault LEDs (commonly red/amber "FLT" or "ERR" per module), and CPU run/stop/fault state in software (RUN / STOP / FAULT / PROG in the status bar).
Frame as the first diagnostic step: hardware/comm fault vs. logic-level fault are different failure domains requiring different next steps.
Triage sequence to teach as a habit:
  1. Check CPU state first — if FAULT, check the fault log/history for a specific fault code before touching logic.
  2. Check module-level LEDs next — a module fault often points to a specific I/O channel or a comms issue on the backplane.
  3. Only after ruling out both, move into online monitoring (3a) to inspect logic-level behavior.
Why order matters: Chasing a logic bug for twenty minutes when the actual problem is a faulted I/O module is a very common, very avoidable waste of troubleshooting time.
Day 2 — Timers, Counters & Troubleshooting
24

## Slide 25
FOLDED INTO BLOCK 3
Project: Forcing Exercise
Force PartSensor high without physical actuation — confirm CTU.CV increments.
Force Fan_Output on/off directly, independent of FanRunOn.Q.
Ask students to state explicitly which fault category (hardware vs. logic) each forcing action would help isolate in a real troubleshooting scenario.
Closing check: Have students locate and clear any forces they created, reinforcing the "always clear your forces" habit from 3b before moving on to Block 4.
Day 2 — Timers, Counters & Troubleshooting
25

## Slide 26
Block 4
Combine Timer + Counter,
Group Troubleshooting
25 minutes

## Slide 27
4A · 10 MIN
Retentive vs. Non-Retentive Timers — RTO
RTO_Instance(IN := MotorRunSignal, PT := T#8h);
ET := RTO_Instance.ET; // accumulates across multiple IN pulses, survives IN going false
RES_Instance(RTO_Instance); // separate explicit reset instruction required
Key distinction: A standard TON's ET/.ACC is implicitly cleared whenever IN goes false. An RTO's ET/.ACC is held across an IN-false period and only cleared by an explicit RES instruction — meaning it can persist even through a PLC power cycle if retentive memory is battery-backed or non-volatile (platform-dependent).
Use case: total motor run-time across multiple start/stop cycles — e.g. preventive maintenance (service every 8 accumulated running-hours, regardless of how many separate times it was started/stopped).
Day 2 — Timers, Counters & Troubleshooting
27

## Slide 28
4A
RTO — Second Use Case & Retentive Counters
Second use case: cumulative machine-cycle time for a shift-based production report — accumulating total "actively producing" time across an 8-hour shift with multiple short stops for material changeovers, where each stop should not erase the running shift total.
Ask students to identify why a plain TON would be unusable here (it would reset to zero on every changeover stop, discarding all previously accumulated time) before revealing RTO as the fix — reinforces the distinction by contrast rather than definition alone.
Retentive counters, briefly: most CTU/CTD instructions are inherently retentive by default (CV holds its value across IN going false, since CU is edge-based rather than level-based).
Contrast explicitly with timers, where retentive behavior is the exception (RTO), not the default (TON). Easy for students to assume the two instruction families behave symmetrically when they don't.
Day 2 — Timers, Counters & Troubleshooting
28

## Slide 29
4B · 10 MIN
Live Debugging Exercise
Pre-plant faults into a working program:
  1. Remove the ONS / R_TRIG in front of a CTU — count increments on a held input.
  2. Swap an RTO for a TON in a cumulative-runtime rung — accumulated value resets unexpectedly every time the motor stops.
  3. An RTO used where a plain TON was actually needed (e.g. a delay-before-alarm rung that should reset cleanly each time the alarm clears, but instead keeps accumulating stale elapsed time because no RES rung exists) — demonstrates retentive behavior is not universally "better," it's situation-dependent, and misuse creates its own bug class.
Method: Have students use Block 3's online monitoring (live rung state, .ACC/ET values, forcing) to localize each fault rather than reading source code top to bottom — mirrors actual field troubleshooting. Diagnostic habit: check the live .ACC/ET value first, compare it against expected behavior, and only then look at the wired logic — numeric-value-first, not logic-read-first.
Day 2 — Timers, Counters & Troubleshooting
29

## Slide 30
4C · 5 MIN
Project: Counter With Built-In Delay
|--[ PartSensor ]--[ONS]--( DebouncePulse )--|
|--[ DebouncePulse ]----------------( TON )--|
Timer: DebounceTimer Preset: 3000 (ms)
|--[ DebounceTimer.Q ]---------------( CTU )--|
Counter: PartCount
State explicitly: the sensor must produce a stable signal for the full 3-second window (the rung as drawn requires the input to remain continuously true, not just pulse). Flag this against the actual simulated sensor behavior — a true debounce-before-count pattern sometimes needs the timer gated differently depending on whether the "noise" is a single glitch or a sustained but jittery signal.
Note the instruction ordering: ONS produces a single pulse that does not feed the counter directly — instead it feeds a TON, and the TON's completion (a stable condition sustained the full preset) feeds the counter. Meaningfully different from Block 2's simple ONS-directly-into-CTU pattern — have students articulate the difference before moving to the Day Project.
Day 2 — Timers, Counters & Troubleshooting
30

## Slide 31
Block 5 — Day Project
Traffic Light Controller
95 minutes
Goal: Red → Green → Yellow → Red, looping, timed by TONs, driven by an explicit state variable.

## Slide 32
State Variable — Two Viable Approaches
Option A — one INT state register (TrafficState, values 0/1/2 for Red/Green/Yellow), compared with EQU instructions to gate each branch.
Option B — three mutually exclusive BOOL bits (State_Red, State_Green, State_Yellow), each set by the prior state's timer completion and cleared by its own timer completion.
Framing point before design begins: Every previous rung this week has been purely combinational — output depends only on the current scan's inputs. A state machine is sequential — output depends on current inputs AND remembered history (which state it's currently in). Name this distinction — combinational vs. sequential logic — explicitly on the board; it's the conceptual leap this project actually tests, not just "more timers."
Day 2 — Timers, Counters & Troubleshooting
32

## Slide 33
Design — 10 min
[Red, TON_Red PT=10s] --Q--> [Green, TON_Green PT=8s] --Q--> [Yellow, TON_Yellow PT=3s] --Q--> back to Red
Sketch the state diagram above on the board first.
Have students annotate, for each state, exactly which output(s) are active and which timer is running — this forces an explicit mapping between "state" (an abstract idea) and "concrete PLC tags" (Red_Light, TON_Red, etc.) before any code is written.
This is where most of the design confusion for a first state-machine project actually originates.
Day 2 — Timers, Counters & Troubleshooting
33

## Slide 34
35 MIN · ALLEN-BRADLEY STYLE
Build — Option A (INT State Register)
|--[ TrafficState EQU 0 ]-----------------------------( Red_Light )--|
|--[ TrafficState EQU 0 ]-----------------------------( TON_Red )--| Preset: 10000
|--[ TON_Red.Q ]--------------------[MOV 1, TrafficState]--( RES TON_Red )--|
|--[ TrafficState EQU 1 ]-----------------------------( Green_Light )--|
|--[ TrafficState EQU 1 ]-----------------------------( TON_Green )--| Preset: 8000
|--[ TON_Green.Q ]------------------[MOV 2, TrafficState]--( RES TON_Green )--|
|--[ TrafficState EQU 2 ]-----------------------------( Yellow_Light )--|
|--[ TrafficState EQU 2 ]-----------------------------( TON_Yellow )--| Preset: 3000
|--[ TON_Yellow.Q ]-----------------[MOV 0, TrafficState]--( RES TON_Yellow )--|
Key mechanism: Note the explicit RES (reset) instruction on each timer at the moment of state transition — this is the exact mechanism that prevents the bug flagged in Test & Debug.
Day 2 — Timers, Counters & Troubleshooting
34

## Slide 35
FOR CONTRAST — BUILD OR SKETCH ALONGSIDE OPTION A
Build — Option B (Three BOOL Bits)
|--[ State_Red ]----------------------------------------( Red_Light )--|
|--[ State_Red ]----------------------------------------( TON_Red )--| Preset: 10000
|--[ TON_Red.Q ]--[SET State_Green]--[RES State_Red]--( RES TON_Red )--|
|--[ State_Green ]--------------------------------------( Green_Light )--|
|--[ State_Green ]--------------------------------------( TON_Green )--| Preset: 8000
|--[ TON_Green.Q ]--[SET State_Yellow]--[RES State_Green]--( RES TON_Green )--|
|--[ State_Yellow ]-------------------------------------( Yellow_Light )--|
|--[ State_Yellow ]-------------------------------------( TON_Yellow )--| Preset: 3000
|--[ TON_Yellow.Q ]--[SET State_Red]--[RES State_Yellow]--( RES TON_Yellow )--|
Note: The explicit SET/RES pair on the state bits guarantees mutual exclusivity only if implemented correctly on every transition — a missed RES on the outgoing state bit is a distinct, additional bug class beyond the timer-reset bug.
Day 2 — Timers, Counters & Troubleshooting
35

## Slide 36
Test & Debug — 35 min
Root-cause of the most common bug: if RES TON_Red is omitted, TON_Red.ET/.ACC is never explicitly zeroed. Depending on platform, a TON whose IN goes false will typically auto-reset ET to 0 the next scan anyway — but if the same instance is reused or the comparison logic overlaps across the transition scan, stale ET values can cause a short first pulse on the next cycle.
Have students verify, using the .ACC/ET monitor from Block 3a, that each timer's accumulated value is genuinely 0 at the exact scan its state becomes active again.
Option B specific bug: forgetting the RES on the outgoing state bit results in two state bits simultaneously true for one or more scans — two lights could briefly both be active. Ask Option B groups to verify, using live monitoring, that exactly one state bit is true at every point in the cycle, never zero and never two.
For the curious (not a required debugging target): if the transition rung and timer-gating rung are evaluated in an order where the state changes mid-scan before the old state's timer rung has run that same scan, some platforms' top-to-bottom single-pass scan order can produce a one-scan glitch depending on rung placement.
Day 2 — Timers, Counters & Troubleshooting
36

## Slide 37
15 MIN + IF FINISHED EARLY
Class Walkthrough & Extension
 | Option A (INT + EQU) | Option B (3 BOOL bits)
Scales to more states | Better — one register regardless of state count | Doesn't scale cleanly past a handful
Readability at 3 states | Requires an EQU comparison per state | More readable
Exclusivity bookkeeping | Avoided by design — only one value can equal a comparison target at once | Needs explicit SET/RES bookkeeping
If finished early: add a PedestrianBtn input that forces TrafficState to a new interrupt state (e.g. state 3 = all-red + walk-signal) regardless of the current normal-cycle state, then returns to state 0 (Red) after its own TON expires.
Requires an explicit priority check at the top of the rung logic — e.g. testing PedestrianBtn before the normal state-transition rungs — a direct preview of priority/override logic needed in more complex sequencing later.
Ask students: should a pedestrian request interrupt an in-progress Green phase immediately, or be "latched" until the current phase naturally completes? Both are defensible (immediate safety response vs. avoiding an abrupt light change to approaching traffic) — no single correct answer; surfacing that ambiguity is itself a useful discussion for a first exposure to interrupt/override design.
Day 2 — Timers, Counters & Troubleshooting
37